## Slide 1
Technical presentation
Measurement and Equipment inspections

## Slide 2
What is needed to enter the championship?
2024 ORC International Certificate
Issued no later than 20 September 2024
CDL between 8.000 and 16.400 (16.401 – 24.000 for Maxi Class)
Flotation date not earlier than 27 September 2019
Stability Index (SI) greater than 103.0
A boat shall have only one valid certificate at any one time. The valid certificate shall be only the one issued last and shall be applied throughout the championship.

## Slide 3
What is needed to enter the championship?
All sails shall be measured
All sails (mainsails, headsails set on the forestay, headsails set flying, symmetric and asymmetric spinnakers) shall be measured according to the IMS Rule.
Storm & heavy weather sails shall be measured according to the WS Offshore Special Regulations (OSR).
All sails shall have a measurement stamp or sticker with all required measurements clearly readable.
Any sail without a measurement stamp or measurements clearly readable, will be needed to be measured at the venue. An appropriate measurement fees will be charged accordingly

## Slide 4
Pre-race equipment inspection schedule
Friday, 27 September 2024
09:00 – 13:00
14:00 – 18:00
Saturday, 28 September 2024
09:00 – 13:00
14:00 – 18:00
Sunday, 29 September 2024
09:00 – 13:00
The measurement appointment form will go live Friday, 30 August.

## Slide 5
How to get prepared for the pre-race inspection?
Be ready at the scheduled time with a responsible person on board (e.g., owner and/or skipper).
Present all sails with the corner taken out from the bag showing the ORC measurement stamp.
Make a clear decision which sails you want to use during the championship.
Have all safety equipment ready for inspection.

## Slide 6
What is checked during the pre-race inspection?
Sails
The maximum number of sails to be used at the event excluding storm & heavy weather sails required by the OSR shall be as defined in ORC Rule 206.1
Each boat shall select sails to be used at the event up to the maximum numbers as defined above. Selected sails will be marked with an event sticker. Only sails marked with an event sticker may be on board during the event.
Sails carried on board may vary from day to day, but shall remain the same for each race day, including days with multiple races even in the case of damage to sails. The race day begins when the boat leaves for the race course from its dock or mooring.
Sails damaged during the event may be repaired. Sails beyond repair may be replaced with permission of the Technical Committee.

## Slide 7
What is checked during the pre-race inspection?
Internal ballast
If there is any, weight and position will be checked.
An internal ballast shall be properly fixed below the cabin sole, or as low as possible fixed to the hull structure to prevent movement.

## Slide 8
What is not checked during the pre-race inspection?
Crew weight
Crew weight is NOT part of the pre-race equipment inspection
Official scale is available for your own check
Crew weight may be checked during the post-race equipment check and if it is found greater than the maximum or smaller than the minimum recorded on the certificate, TC will protest the boat
Be sure to have your crew weight properly declared on the certificate.

## Slide 9
What is checked during the pre-race inspection?
Safety equipment
Download the safety equipment check list at the link.
Be sure to have ALL equipment from that list, but please be aware that the check list does not cover ALL rules of OSR.
The full compliance with OSR Category 3 (as amended by the NOR) is the sole responsibility of the person in charge and it cannot be limited to the safety check list

## Slide 10
Safety equipment
Navigation lights
mounted above sheerline and so that they will not be masked by sails or the heeling of the boat.
  Minimum 10 w (if incandescent) for LOA<12 m
  Minimum 25 w (if incandescent) for LOA≥12 m
reserve lights having the same specifications as above, and that can be powered independently
spare bulbs (not required for LED)

## Slide 11
Safety equipment
Marine VHF transceiver
a marine radio transceiver with an emergency antenna when the regular antenna depends upon the mast
If VHF: minimum rated output power of 25 W
a masthead antenna and co-axial feeder cable with not more than 40% power loss
VHF radio transceiver shall be capable of operating in “US Mode”

## Slide 12
Safety equipment
AIS Transponder which either:
  shares the masthead VHF antenna via a low loss AIS antenna splitter; or
  has a dedicated AIS antenna not less than 38 cm (15”) in length mounted with its base not less than 3 m (10’) above the Waterline and co-axial feeder cable with not more than 40% power loss
  The boat’s AIS shall be active at all times while racing.

## Slide 13
Safety equipment
Soft tapered wood plugs
  A tapered soft wood plug stowed adjacent to every through-hull opening

## Slide 14
Safety equipment
Fire extinguishers
  A fire blanket adjacent to every cooking device with an open flame
  2 fire extinguishers, each with 2 kg (4 lbs) of dry powder or equivalent, in different parts of the boat

## Slide 15
Safety equipment
Flashlight and Searching light
  a searchlight, suitable for searching for a person overboard at night and for collision avoidance
  a watertight flashlight
  spare batteries and bulbs for both

## Slide 16
Safety equipment
First Aid Kit & Manual
  A First Aid Manual and First Aid Kit. The contents and storage of the First Aid Kit shall reflect the likely conditions and duration of the passage, and the number of crew

## Slide 17
Safety equipment
Foghorn, rigging cutter and knife
  A Foghorn
  An effective means to quickly disconnect or sever the standing rigging from the boat
  A knife readily accessible from thedeck or a cockpit

## Slide 18
Safety equipment
Radar reflector
  A passive radar reflector with:
    octahedral circular plates of minimum diameter 30 cm (12”), or
    octahedral rectangular plates of minimum diagonal dimension 40 cm (16”), or
    a non-octahedral reflector with a documented Root Mean Square minimum Radar Cross Section (RCS) area of 2 m2 (22 ft2) from 0-360° of azimuth and ±20° of heel

## Slide 19
Safety equipment
Charts and Compass
  Navigational charts (not solely electronic), light list and chart plotting Equipment
  Marine magnetic compass capable of being used as a steering compass:
  Permanently installed marine magnetic steering compass, independent of any power supply, correctly adjusted with deviation card
  Second compass which may be hand-held and/or electronic

## Slide 20
Safety equipment
Pyrotechnics
  Pyrotechnic signals shall be provided conforming to SOLAS LSA Code Chapter III Visual Signals and not older than the stamped expiry date (if any) or if no expiry date stamped , not older than 4 years:
    4 Red Hand Flares
    2 Orange Smoke Flares

## Slide 21
Safety equipment
Bilge pump and buckets
  Two strong buckets, each with a lanyard and of at least 9 liters (2.4 US Gal) capacity
  One permanently installed manual bilge pump
  All required permanently installed bilge pumps shall be operable with all cockpit seats, hatches and companionways shut and with permanently installed discharge pipe(s) of sufficient capacity
  All removable bilge pump handles retained by a lanyard

## Slide 22
Safety equipment
Anchors
  2 un-modified anchors that meet the anchor manufacturer’s recommendation based on the boat’s dimensions with suitable combination of chain and rope, ready for immediate assembly, and ready for deployment within 5 minutes

## Slide 23
Safety equipment
Lifejackets
  Each Crew Member shall have a lifejacket which shall:
  have an emergency position indicating light, whistle, lifting loop, automatic/manual gas inflation system
  be clearly marked with the boat’s or wearer’s name
  have a sprayhood in accordance with ISO 12402-8
  A boat shall carry at least one gas inflatable lifejacket spare cylinder and, if appropriate, spare activation head for each type of lifejacket on board
Life Jackets shall be worn on deck between 18:00 and 07:00

## Slide 24
Safety equipment
Tethers
  Each Crew Member shall have a tether that shall:
    a tether not exceeding 1m(3'3") including the length of the hooks, or
    an intermediate self-closing hook on a 2 m (6’-6”) tether
  have self-closing hooks
  have overload indicator flag embedded in the stitching
  be manufactured after 2000

## Slide 25
Safety equipment
LIfebuoy
A lifebuoy with:
A self-igniting light
a whistle
a drogue
within reach of the helmsman and ready for immediate use

## Slide 26
Safety equipment
Heaving line
A heaving line, no less than 6 mm (1/4")diameter, 15 - 25 m (50 - 75’) long, readily accessible to cockpit

## Slide 27
Safety equipment
Recovery sling
A recovery sling which includes a:
  buoyant line of length no less than the shorter of 4 times LOA or 36m (120’)
  buoyancy section (horseshoe) with no less than 90 N (20#) buoyancy
  minimum strength capable to hoist a crewmember aboard

## Slide 28
Safety equipment
Lifelines
Lifelines of stranded stainless-steel wire (Min. 4 mm 8.5<LOA≤13; Min.5 mm LOA>13 m)
Dyneema lifelines are not allowed
When a deflecting force of 4 kg is applied to a lifeline at the mid-point of the longest span between supports that are aft of the mast, the deflection shall not exceed:
  50 mm (2”) for an upper or single lifeline
  120 mm (4 ¾”) for an intermediate lifeline
  Stainless steel lifelines shall be uncoated
  A lanyard of synthetic rope may be used
  to secure lifelines provided the gap it
  closes does not exceed 100 mm

## Slide 29
Safety equipment
Jackstays
Jackstays shall:
  be independent on each side of the deck
  enable a crewmember to move readily between the working areas on deck and the cockpit(s) with the minimum of clipping and unclipping operations
  have a breaking strength of 2040 kg (4500#) and be uncoated and non sleeved stainless steel 1 x 19 wire of minimum diameter 5 mm (3/16”), webbing or HMPE rope
  Jackstays need to be mounted on the deck for the offshore races only from the moment when the boat is leaving the dock.

## Slide 30
Safety equipment
Clipping points
Clipping points shall:
  be adjacent to stations such as the helm, sheet winches and masts, where crewmembers work
  enable a crewmember to clip on before coming on deck and unclip after going below

## Slide 31
Safety equipment
Storm and Heavy weather sails
  A Heavy Weather Jib with:
    area not greater than 13.5% height of the foretriangle squared
    readily available means, independent of a luff groove, to attach to the stay
Either a storm trysail as defined in OSR 4.26.2 d), or mainsail reefing to reduce the luff by at least 40%
  A storm trysail with no headboard, no battens
  The material of the body of a storm sail purchased after 2013 shall have a highly-visible color (e.g. dayglo pink, orange or yellow)
  Storm and Heavy weather sails shall be measured

## Slide 32
Safety equipment
Emergency tiller
An emergency tiller capable of being fitted to the rudder stock except when:
the principal method of steering is by means of an unbreakable metal tiller
there are two methods (e.g. tillers, wheels) of controlling a rudder, neither of which shares components with the other except for the rudder stock
A proven method of emergency steering with the rudder disabled

## Slide 33
What is checked after racing?
On the water
TC members will approach boats selected randomly
The following will be inspected after each inshore race:
  the presence of event stickers on the sails on board
  the position of the items recorded in the measurement inventory
  major OSR compliance (such as the tension of the lifelines).

## Slide 34
What is checked after racing?
At the dock – After the long offshore race
Safety equipment and the presence of event stickers on the sails on board among randomly selected boats in each class.

## Slide 35
What is checked after racing?
At the dock – After inshore races
Flotation: 1st boat overall in each class when selection is made.
Sails measurements check: 2nd boat overall in each class when selection is made. The largest of each will be checked: mainsail, headsail set on the forestay, symmetric spinnaker, asymmetric spinnaker, all headsails set flying and all asymmetric spinnaker with SHW/SFL < 85%.
Crew weighing 3rd boat overall in each class when selection is made. The Crew shall be weighted in light street clothes with short trousers, a t-shirt, and flip-flops as a minimum.

## Slide 36
What is checked after racing?
At the dock – After inshore races
These criteria shall be applied at the end of each racing day, except when the boat is supposed to be inspected for an item previously checked. In this case, a different check may be scheduled for that boat, and if needed, boats placed 4th, 5th, 6th etc. will be inspected.
Independently from the results, any boat can be inspected upon a measurement protest or by the choice of the Technical Committee.

## Slide 37
What can be the result of the post-race inspection?
If the Technical Committee finds that boats do not comply with the ORC Rating Rules, it shall protest the boat, and it may protest the boat for any infringement of the OSR.
The flotation check will start with the freeboards measurement. A test certificate will be run with these measurements to calculate APH that will be compared with the one on your ORC International certificate.
If the difference between the two APHs is less than 0.1%, a boat will be considered in compliance with her certificate. If the difference is greater, an inclining test will be performed to run a new test certificate.
If the APH difference is still greater than 0.1%, TC will protest the boat and ORC Rule 305.2 will be applied.

## Slide 38
What can be the result of the post-race inspection?
If there is any difference in sail measurements, a test certificate will be run with these sail measurements for a comparison of the APH with the one on your ORC International certificate. If the APH difference is greater than 0.1%, TC will protest the boat and ORC Rule 305.2 will be applied.

## Slide 39
What can be the result of the post-race inspection?
If the crew weight is found greater than the maximum or smaller than the minimum recorded on the ORC International certificate, TC will protest the boat.
Please note that ANY infringement related to the crew weight is not considered as an issue of compliance with the certificate and it is not subject to the APH comparison.
Please remember that you may declare maximum crew weight and add safety margin to be sure that crew complies with the rule.
ORC Rule 305.2 does not apply in this case, and the decision of the protest may be a disqualification in all races where crew weight was not in the range given in the certificate.
The same principle applies for other tow items that may be declared by the owner: use of asymmetric spinnaker tacked on the centerline only and adjusting the mast foot while racing

## Slide 40
What can be modified during the championship?
Crew changes: Once the entry is accepted, each boat shall submit the crew list that shall include all crew members who will be on board at the start of the first race
After the first race, changes in crew (adding new crew members, replacing, or disembarking crew members) shall be notified to the race office.
Crew changes will be automatically approved provided that crew weight after the change is within the limits defined in the ORC certificate
The substituted crew member shall not be aboard any other competing boat throughout the remainder of the series.

## Slide 41
What can be modified during the championship?
Equipment changes: Substitution of damaged or lost equipment is not allowed unless authorized by the Technical Committee.
Requests for substitution shall be made at the first reasonable opportunity.
If this includes sails damaged beyond repair, please present the damaged sail to the Technical Committee.

## Slide 42
Any questions?